Pulsar simulation with PSRPopPy
Adam D

---
Procedure
Apply radiometer equation to calculate SNR (using SNR cut off 9)
Calculate gain + observation time for each pulsar location
Generate order 100000 Pulsar

---
Results
- 118122 pulsars simulated
- See order ~2000 , the number deviates everytime by ~100
- Order ~20000 too faint
- Order ~20000 smeared
- Order ~70000 not in CHIME sky region
- (showing 1796 pulsars detected, 25754 too faint, 19841 smeared, 70731 not in sky region)

---
Luminosity distribution
Log norm [-1.1,0.9]

---
Parameters
- Duty percent = 6%
- Scindex = - 3.86 – spectral index of scattering model
- Radial distribution type=lfl06
- SiDistPars=[-1.6,0.35] mean, sig – Gaussian
- Period dist = [2.7,-0.34] mean, sig – log norm
- Radiometer single pulse eq:
  - Where S_sys = T_sys/gain
  - Beta is the telescope degredation factor =1
SNR = c times sqrt{n_p times bw times w} times S_{max} over {S_{sys} times beta }

---
- 1.0 ! survey degradation factor
- 1.16 ! antenna gain (K/Jy)
- 641. ! days on sky (CHIME specific parameter)
- 1. ! sampling time (ms)
- 60. ! system temperature (K)
- 600. ! centre frequency (MHz)
- 400. ! bandwidth (MHz)
- 0.244140625 ! channel bandwidth (MHz)
- 2 ! number of polarizations
- 17.18 ! full-width half maximum (arcmin)
- 0. ! minimum RA (deg)
- 360. ! maximum RA (deg)
- -20. ! minimum DEC (deg)
- 90. ! maximum DEC (deg)
- -180. ! minimum Galactic longitude (deg)
- 180 ! maximum Galactic longitude (deg)
- 0. ! minimum abs(Galactic latitude) (deg)
- 90 ! maximum abs(Galactic latitude) (deg)
- 1. ! fractional sky coverage (0-1)
- 9.0 ! minimum signal-to-noise

---
Results
- See order ~1000 rrats, the number deviates everytime by ~100
- Order ~1 doesn’t burst while CHIME is watching
- Order ~10000 too faint
- Order ~10000 smeared
- (showing 1302 rrats detected, 3 didn’t burst, 21939 too faint, 16838 smeared)

---
Generating properties
Lum distribution – Faucher-Giguere, Kaspi 2006 (blue is the generated population, orange is the portion detected by CHIME) – log norm [-1.1,0.9]
This bar goes higher

---
Mean -1.6 sigma 0.35
Uniform log distribution, low 0.1, high 3

---
GAINS AND OBSERVATION TIMES
(# OF RRATS DETECTED BY CHIME)

---
Giant pulses?
Apply radiometer equation to calculate SNR (using SNR cut off 9)
Check period and how many GPs is emitted
Draw from a luminosity distribution derived from crab
Assume a fraction of periods have GPs
Calculate gain + observation time for each pulsar location
Simulate a population of pulsars based on PMSURV

---
Results- 113474 pulsars simulated
- See order ~900 GP emitters, the number deviates everytime by ~100
- Order ~0 too faint
- Ignoring smearing
- (showing 902 GP detected, 44290 don’t do GP, 68282 not in region)

---
- Period drawn from log norm dist
- GP lum drawn from double power distribution (Popov et al. 07)
- Blue line shows pulsar normal luminosity
- Orange line show giant pulse luminosity that has been detected by CHIME FRB
I just did a cut off

---
To do
- Get radiometer equation constants from injections
- Draw fraction of periods that emit GP from same distribution as lum
- Get a wider range of luminosities from more than just Crab
- GP cut off – light cylinder
- Compare with actual CHIME results